## Slide 1
The Energy Saving Potential of Balancing PECS and Background system on Light under Changing Occupancy
– A Case Study on BEEHub Historical Data
25Fall BPS5231 AI for Sustainable Building Design
Kefan Chen, Guanli Feng
Nov 19, 2025

## Slide 2
Problem Description
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Results

## Slide 3
Problem Identification
Background system –> general space control PECS –> micro-environment of occupants
➡️ And occupants come and leave ➡️ controlling strategy -- changing occupancy condition?
Research Question/Hypothesis
1 > Optimization on light control and energy?: different occupant distribution Balancing PECS and background system control on lighting ➡️ visual light comfort ⬇️ lighting energy consumption
2 > Case study on real occupancy historical data of BEE Hub: Could we utilize ML tools (like surrogate model thinking) to apply such control strategy on different occupant distribution in an accurate and low time-consuming way? Then we could combine it with historical occupancy data to visualize its energy saving potential.
Tekler, Z.D., Ono, E., Peng, Y. et al. ROBOD, room-level occupancy and building operation dataset. Build. Simul. 15, 2127–2137 (2022). https://doi.org/10.1007/s12273-022-0925-9
GPT5-generated diagram
Problem Description
Notes: The bg system is for general overall space control
PECS, that is .., like – desk fan, task light – is for micro-environment control of individuals – a question of how to balance using them
Meanwhile people come and leave the space, so we wanna explore a dynamic controlling strategy by simulation that if there’s a way to maintain visual light comfort and save energy consumption while occupancy condition keeps changing

## Slide 4
Problem Description
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Results

## Slide 5
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 6
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 7
(a) Environmental inputs of BEE Hub
Occupancy distribution: Randomly generate occupant distribution on designed seats (max possibility= 2^n, n = 24)
3D model: BEE Hub
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Notes: For env input, they are occupancy distribution and 3D space model

## Slide 8
(a) Environmental inputs of BEE Hub
Occupancy distribution: Randomly generate occupant distribution on designed seats (max possibility= 2^n, n = 24)
3D model: BEE Hub
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Notes: And basic layout is like this. U can see the tables, the ceiling lights, and table task lights

## Slide 9
(b) Decision variables
Background system & Task light: Level inputs of ceiling and task lights – Lumen & Power
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Notes: For decision variables which we wanna find best setings, they are the light level of ceiling light and table task light
The two types light that we are currently using are both with very low energy standard so we took them as example. All power and lumen data we use for simulation are from official booklet

## Slide 10
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
(b) Decision variables
Background system & Task light: Level inputs of ceiling and task lights – Lumen & Power
Notes: So we could put all factors and start simulating

## Slide 11
(c) Objective variables
Light energy consumption: The parameter that we want to minimize
Visual light comfort: Quantify from electric lighting simulation The restriction we need to follow
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Notes: The objective variable that we do optimization based on is the energy consumption and light comfort. Here is how to calculate comfort, the work surface illuminance and uniformity

## Slide 12
(c) Objective variables
Light energy consumption: The parameter that we want to be lower
Visual light comfort: Quantify from electric lighting simulation The restriction we need to follow
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 13
(d) Optimization Min(Power + Penalty (luminance and uniformity))
Galapagos Algorithm
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Notes: we combine the power with comfort result. The comfort part works as the penalty term, then we get such formulation. Then we use Galapagos in gh to minimize the total sum by search the best way of controlling all the lights

## Slide 14
(e) Optimized result
The balanced light control strategy based on inputted occupant distribution
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Notes: So it’s like the ceiling light will affect different and how to arrange them in a better way
Then we can results, and output them as one training pair

## Slide 15
(f) Training dataset pairs
The balanced light control strategy based on inputted occupant distribution (1094 pairs)
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Lighting control – Occupant distribution
Notes: Later we loop the process and get the over 1k training dataset pairs, that are the occupant distribution and the corresponding light control

## Slide 16
(g) Train surrogate model
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Image Input:
RGB Plan image of seat occupancy
Tabular Input:
Occupant Count + Seat Occupancy
Notes: Multimodal deep learning model
Image part: CNN
Tabular part: MLP
Fusion MLP

## Slide 17
(g) Train surrogate model
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
3 features 256*256
Image Branch:
Maxpool
Maxpool
Maxpool
64*64
128*128
32*32
AdaptiveAvgPool
64 features 4*4
Flatten
1024 features
Notes: 3 channels of RGB
Several steps of Conv. & Pooling to 1024 features

## Slide 18
(g) Train surrogate model
Outputs: 24 task illuminance levels + 3 ceiling light illuminance levels + power
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Tabular Branch:
25 dimensions: occupant_count + occupancy at 24 seats
Fusion MLP:
1088
256
128
28
Feature Embedding
64 features
1024 features
Notes: Tabular data: feature embedding to 64 features
1088 features to MLP
28 outputs

## Slide 19
(g) Train surrogate model
Optimizer: Adam
Loss Function: MSE
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
BATCH_SIZE = 32
NUM_EPOCHS = 300
LEARNING_RATE = 1e-3
VAL_SPLIT = 0.2
BATCH_SIZE = 32
NUM_EPOCHS = 200
LEARNING_RATE = 1e-3
VAL_SPLIT = 0.2
Notes: Epoch = 300, convergence goes well

## Slide 20
(h) Case test on historical data
The occupancy data of BEE Hub (link) Then apply trained surrogate model and compare the energy performance with solely use background light
Average occupant count for BEE Hub on an average day. Tekler, Z.D., Ono, E., Peng, Y. et al. ROBOD, room-level occupancy and building operation dataset. Build. Simul. 15, 2127–2137 (2022). https://doi.org/10.1007/s12273-022-0925-9
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Notes: Use the actual occupancy data to test the results

## Slide 21
Problem Description
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Results – Saving potential

## Slide 22
Results – Saving potential
Tekler, Z.D., Ono, E., Peng, Y. et al. ROBOD, room-level occupancy and building operation dataset. Build. Simul. 15, 2127–2137 (2022). https://doi.org/10.1007/s12273-022-0925-9
Occupancy could be high in some nights at BEE hub
Maximum occupancy of seats is 10 during the study period
Total energy use: Optimized power from 39.92 kWh to 34.72 kWh in 285 hours in total

## Slide 23
Results – Saving potential
Previous Power: ceiling light control only
Simple Combined: 5-level desk light + 3-level ceiling light at the seats occupied
Optimized Power: Prediction by ML model
Conclusion:
Compared to previous power, simple combined and optimized power can significantly decrease the lighting power (55.5% and 68.3% respectively)
Optimized Power generally performs better than Simple Combined except 1-person occupancy.

## Slide 24
Results – Saving potential
Overall the Optimized Power perform better than the other two.
Limitation: The predictions at low occupancy are often not optimal.
Future work: fix the inaccuracy at lower occupancy; incorporate daylighting simulation

## Slide 25
Thanks:)