## Slide 1
The Energy Saving Potential of Balancing PECS and Background system on Light
– A Case Study on BEEHub
25Fall BPS5231 AI for Sustainable Building Design
Kefan Chen, Guanli Feng
Nov 19, 2025

## Slide 2
Problem Description
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Results

## Slide 3
Problem Identification
Background system –> general space control PECS –> micro-environment of occupants
➡️ But occupants come and leave ➡️ controlling strategy -- changing occupancy condition?
Research Question/Hypothesis
1 > Optimization on light control and energy?: different occupant distribution Balancing PECS and background system control on lighting ➡️ visual light comfort ⬇️ lighting energy consumption
2 > Case study on real occupancy historical data of BEE Hub: Could we utilize ML tools (like surrogate model thinking) to apply such control strategy on different occupant distribution in an accurate and low time-consuming way? Then we could combine it with historical occupancy data to visualize its energy saving potential.
Tekler, Z.D., Ono, E., Peng, Y. et al. ROBOD, room-level occupancy and building operation dataset. Build. Simul. 15, 2127–2137 (2022). https://doi.org/10.1007/s12273-022-0925-9
GPT5-generated diagram
Problem Description

## Slide 4
Problem Description
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Results

## Slide 5
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 6
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 7
(a) Environmental inputs of BEE Hub
Occupancy distribution: Randomly generate occupant distribution on designed seats (max possibility= 2^n, n = 24)
3D model: BEE Hub
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 8
(b) Decision variables
Background system & Task light: Level inputs of ceiling and task lights – Lumen & Power
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 9
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
(b) Decision variables
Background system & Task light: Level inputs of ceiling and task lights – Lumen & Power

## Slide 10
(c) Objective variables
Light energy consumption: The parameter that we want to minimize
Visual light comfort: Quantify from electric lighting simulation The restriction we need to follow
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 11
(c) Objective variables
Light energy consumption: The parameter that we want to be lower
Visual light comfort: Quantify from electric lighting simulation The restriction we need to follow
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 12
(d) Optimization Min(Power + Penalty (luminance and uniformity))
Galapagos Algorithm
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 13
(e) Optimized result
The balanced light control strategy based on inputted occupant distribution
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 14
(f) Training dataset pairs
The balanced light control strategy based on inputted occupant distribution (1094 pairs)
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Lighting control – Occupant distribution

## Slide 15
(g) Train surrogate model
Use ML tools
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
FOR GUANLI模型原理解释 可以用Netron
Model structure
类似这样示意一下
图片+座位

## Slide 16
(g) Train surrogate model
Training
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
BATCH_SIZE = 32
NUM_EPOCHS = 300
LEARNING_RATE = 1e-3
VAL_SPLIT = 0.2
BATCH_SIZE = 32
NUM_EPOCHS = 200
LEARNING_RATE = 1e-3
VAL_SPLIT = 0.2

## Slide 17
(h) Case test on historical data
The occupancy data of BEE Hub (link) Then apply trained surrogate model and compare the energy performance with solely use background light
Average occupant count for BEE Hub on an average day. Tekler, Z.D., Ono, E., Peng, Y. et al. ROBOD, room-level occupancy and building operation dataset. Build. Simul. 15, 2127–2137 (2022). https://doi.org/10.1007/s12273-022-0925-9
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case

## Slide 18
Problem Description
Methodology – Optimize control strategy, Create Dataset, Train surrogate model, Apply to physical case
Results – Saving potential

## Slide 19
Results – Saving potential
Tekler, Z.D., Ono, E., Peng, Y. et al. ROBOD, room-level occupancy and building operation dataset. Build. Simul. 15, 2127–2137 (2022). https://doi.org/10.1007/s12273-022-0925-9

## Slide 20
Results – Saving potential
FOR GUANLI
Results after optimized
saving potential visualization, compare with
Like in all
Under different occupant count, etc.
+ how’s the model

## Slide 21
Thanks:)